## Slide 1
WP5 Review
USE CASE 1: Crowdsourced video broadcasts

## Slide 2: Use Case Features
Crowd sourced video streaming
  Enable crowd sourced live video streaming services to scale over large numbers (>1000 users)
Challenges
  Currently all user generated videos are encoded and streamed to a centralised data centre where the video streams are processed.
  Network bandwidth and latencies affect scaling to large user numbers
  Increase in cost(BW), latency(encoding, processing, decoding) and computing resources at DC
Goal
  Not all videos are useful e.g: spectators from the same area pointing cameras at same locations (location aware streaming). So need a system to decode video stream metadata and decide which streams are useful
  Reduce cost and delays by providing computing capability as close as possible to the video streams
  Orchestrate network resources with virtual network/video functions
  Provide a slice for video streaming application owner to manage access control to video streams

## Slide 3: Crowdsourced video streaming
The use case requires following network orchestrator capabilities to host the service:
Computing capability on the fly to aggregate and form clusters of crowd videos at the access network
Provide dynamic high capacity paths to upload clustered video streams
Platform to monitor and gather video application requirements and provide network services. E.g. as the number of video clusters allocate more paths to different cloud locations
Platform to provide virtual load balancers. Capabilities include layer4/7 load balancing, content caching and compression, TCP/IP multiplexing.
Metro Network
Access Network
Stadia 2
Stadia 1
DC1
DC2
video data
Core Network
Video Function
DPI, Firewall
Orchestration (OSM)
Transport SDN controller
Metro & Core
Access SDN controller
DC SDN controller
VIM
WIM
VIM
OpenConfig

## Slide 4: Planned demo scenario
Simulated Stadium 2
Stadium 1
OSM (Orchestration)
Transport SDN controller
Metro & Core
Access SDN controller
University of Bristol
Reading
BT Adastral
AMEN
AMEN
MCEN
OpenStack
Dark Fibre Infrastructure(NDFIS)
Video encoding/ NAC
Video encoding/ NAC
Video Clustering
DC SDN controller
Access/DC SDN control
Transport SDN control
Openstack control

## Slide 5: UC1 Demo elements

## Slide 6: First crowdsource demo @ TIP conference

## Slide 7: First Metrohaul UC1 demo @ TIPSummit18

## Slide 8
video data
Crowdsource Video Slice
DC
NAC
NAC: Network Access Control
Metro Network
Access Network
Stadia 2
Stadia 1
Crowd source DC
Crowd source DC
Core Network
Firewall
DPI
Orchestration & Slicing

## Slide 9: Demo highlights
Service(Video streams) orchestration over dis-aggregated networks
Service orchestration using OSM (VIM and WIM enablers)
  Spawn VNFs (DPI, Firewall & Video function)
  Stitch VNFs with network resources(accesstransportDC)
Slice based service over dis-aggregated networks
MH1,2,3 &8 optical, E2E path connection time with reduced capex

## Slide 10
Physical Topology View
Orchestration View: Connectivity services
Slice View

## Slide 11
Reading/Adstral
Bristol
OSM & Slicing
Transport SDN controller
Metro & Core
OpenStack
Voyager1
Voyager2
VNFs
10G
10G
100G
10G
2*200G
VNFs
10G
10G
100G
10G
WIM
OpenConfig/ NCLU
Camera Port
VR port
VLAN A/B/C…
Node V1
Port, Transport
Camera Port
VR port
VLAN A/B/C…
Node V2
Port, Transport
OXC
OXC

## Slide 12: Demo Architecture
voyager
stadium
BT
SW
Edge video analysis
Zeetta
Transp. Contr.
ONOS
Contr.
Zeetta Controller
T-API
T-API
Ericsson/CNIT
λ-sw
ROADM
(WSS)
voyager
OpenROADM
OpenConfig
OpenROADM Agent
Zeetta
Acc. Contr.
Zeetta
Acc. Contr.
OSM
OpenROADM Agent
L2-SM
Transmission performance monitoring? (Nokia)

## Slide 13: Hardware Details WP3
Component ID | Components | Lead Partner
D4 | Innovative photonic integrated optical switching solution for add/drop module of ROADM | TEI/CNIT
D12 | Programmable packet switching solution for interconnection of access and core segments | Bristol
D19 | Voyager Muxponder | BT/ Bristol
D21 | Bristol ROADM | Bristol
MDA | Agents for Monitoring and Data Analytics | UPC

## Slide 14: Software Details WP4
Component ID | Components | Lead Partner
5.1.1 | Parent SDN Controller | TID
5.1.2 | ONOS Optical Controller | CTTC
5.1.3 | ONOS TAPI 2.1 SBI Driver | TID
5.1.4 | ONOS OC Driver | CTTC+CNIT
5.3.1 | Generic OpenConfig Agent | CNIT, CTTC
5.4.3 | OSM with WIM Plugin | Bristol +TID
5.6.1 | MDA Controller | UPC
5.6.2 | MDA Agent | UPC
5.7.1 | Front-end Net2Plan interfaces | UPCT

## Slide 15: Crowdsource application

## Slide 16: University of Bristol – BT Connection (Dark Fibre)
University of Bristol – BT (Ipswich) Link:
  530km of dark fibre
  Amplified link with optical filters in Cambridge.
  Performance:
    PM-QPSK (100Gb/s): 3.2E-9 (BER BT-Bristol), 8.2E-8 (BER Bristol-Ipswich) @Wavelength 1554.94nm.
    Measured Latency 5.5ms (RTT)
Newmarket
University of Cambridge
Bury St. Edmunds
Adastral Park
BT
Ipswich
University of Bristol
HPN
Bradley Stoke
Froxfield
Reading
Powergate
Telehouse
Duxford
36.24km
24.1km
45.5km
14.2km
30.5km
98.1km
35.2km
77km
51.3km
94.6km
23.6km

## Slide 17
UC1 Challenges
Using Stadium WiFi a big hurdle
  Radio Spectrum utilization
  Scale: simultaneous connections
Crowd source application work
  https streaming: Work required from video app vendor to allow us to identify streams
BT to UoB link

## Slide 18: Next Steps
Preparation for Bristol demo in collaboration with UoB/BT/TIM involving work on the following tasks:
  Openstack and Packet Switch for DC configuration; NFV deployment with openstack.
  NetOS SDN controller and packet switch integration
  OSM and WIMconnector development.
  DC compute node at BT site to provide; Configured by Zeetta and UoB
  NetOS and voyager integration and testing
  ONOS and ROADM integration and testing in NDFIS network
  NetOS and ONOS integration and implementation with OPENCONFIG
  Network service definition and NFV setup
  Crowdsourcing video streaming development efforts

## Slide 19: BACKUP SLIDES

## Slide 20: High Level Plan for demo submission
OFC submission

## Slide 21: 2.4G vs 5G spectrum utilization at Stadium

## Slide 22: Crowd source app GUI

## Slide 23: Plan B: Demo extension to Live 360’ cameras